## Slide 1: IAM Approach to Line Pressure Surveillance
August 22nd, 2018

## Slide 2: Agenda
Background / History
Workflow Steps
Workflow Outputs
Physics Based Modeling
  IPR/VLP & Mach Number
JMZ 1C-3HZ Model
  Early Life & Today
Economic Benefits
Path Forward

## Slide 3: Background / History
Lower line pressure has always been desired by production
  High Impact during summer due to compressors
  Pressure equals money:
    Pressure Increase = Production Decrease & Deferred Revenue
    Pressure Decrease = Expenditure & Capital Spend
    Need to find the equilibrium point between the two
Historically no good way of quantifying the problem
  Too many wells & variables
Insufficient clear data for gathering commitments
  Contracts need to be clearly defined (i.e: What pressure at with what volume?)
During summer months potential value estimated for APC:
  +/-2,000 bpd and +/-$11MM @ $60/bbl

## Slide 4: Elevating the IOC & Field Operations
Real time oil / gas opportunity loss analysis by well
Enhanced daily & weekly IOC reporting
Turn compression on earlier & enhanced KMOG/WES alignment
High backpressure inside the production facility
Identifying high pressure ‘quadrants’ of the field
Identifying wells that are flowing in subsonic flow that are more susceptible to line pressure increases
Workflow programmed to pull historical line pressure averages by production battery
Data support in KMOG/WES contract discussions
Piping and control valve modifications to reduce wellhead back-pressure
Tune wellhead telemetry to increase production

## Slide 5: Workflow 1 Steps
Pull Tubing Pressure, XMV Pressure & Sales Line Pressure
Filter Bad Data From Pressures
Pull Downtime Codes From PDB
Associate downtime codes with pressure timestamps
Delete Pressures associated with planned avoidable
Break Pressures up into 6 hour increments
Flag trends w/ positive slope & w/ >15% increase
Bin pressures into 50 psi increments
Calculate Delta between XMV & Sales Line pressures

## Slide 6: Workflow 2 Steps
Pull exception flags for all wells
Pull production yesterday and production targets
Get production deltas for days w/ exceptions
Multiply deltas by commodity prices
Sum deficits for wells and field by day and week

## Slide 7: XMV Pressure Exception
Pressure Bins
Pressure Deltas
Daily Deferred Volumes & Sales
Weekly Deferred Volumes & Sales

## Slide 8: Flagged Pressure Exception
Oil Goal
Oil Yesterday
XMV Pressure
Gas Sales Pressure
Flagged Pressure
Flagged pressure increase and production Delta

## Slide 9: Flagged Pressure Exception
Oil Goal
Oil Yesterday
XMV Pressure
Gas Sales Pressure
Flagged Pressure

## Slide 10: XMV to Gas Sales Line Delta
Sorted by pressure delta

## Slide 11: XMV to Gas Sales Line Delta
+/-60 psi Delta
Potential to lower pressure upstream of gas sales

## Slide 12: Inflow Performance Relationship
Relationship Between:
  Reservoir Pressure
  Flowing Bottom Hole Pressure
  Production Rate
Stable in conventional plays
  Sand Stone, etc.
Dynamic in unconventional plays
  Shale, etc.
Reservoir Pressure (psig)
Production Rate (bpd)
IPR can change rapidly in shale plays

## Slide 13: Vertical Lift Performance Relationship
VLP: Relationship between bottom hole & surface
  How production flows from bottom hole to surface
Dependent on:
  Well Depth
  Tubing Size
  Water Cut
  GOR
  PVT Properties
  Surface Pressure
Reservoir Pressure (psig)
Production Rate (bpd)
Increase surface Pressure shift up
Decrease surface pressure shifts down

## Slide 14: Combining IPR & VLP
Reservoir Pressure (psig)
Production Rate (bpd)
qp
qp
qp
Intersection is operating point.
Changes in surface pressure change production rates with all other variables held constant

## Slide 15: Compressible Flow
Gas at subsonic flow acts like an incompressible fluid
  If line pressure goes up, well head pressure goes up
Gas at supersonic flow acts like a compressible fluid
  If line pressure goes up, well head pressure isn’t effected

## Slide 16: XMV Pressure Sensitivity Example 1
Early life doesn’t show signs of production decrease until XMV pressure of +/-1,250 psi
Doesn’t load until XMV pressure of +/-2,750 psi

## Slide 17: XMV Pressure Sensitivity Plot Example 2
Doesn’t load up until XMV pressure of +/-2,000 psi
Current day production decrease at +/-650 psi

## Slide 18: Economics – Line Pressure Impact

## Slide 19: Economics – Line Pressure Impact
Line pressure increase cause of plunger exceptions
Total of +/-$1.3MM deferred for week when average is +/-$800k for line pressure

## Slide 20: Economics – Line Pressure Impact
Remains high even after line pressure goes down
Total of +/-$1.1MM Deferred for week when average is +/-$750k

## Slide 21: Elevating the IOC & Field Operations
Real time oil / gas opportunity loss analysis by well
Enhanced daily & weekly IOC reporting
Turn compression on earlier & enhanced KMOG/WES alignment
High backpressure inside the production facility
Identifying high pressure ‘quadrants’ of the field
Identifying wells that are flowing in subsonic flow that are more susceptible to line pressure increases
Workflow programmed to pull historical line pressure averages by production battery
Data support in KMOG/WES contract discussions
Piping and control valve modifications to reduce wellhead back-pressure
Tune wellhead telemetry to increase production

## Slide 22: Path Forward
Run macro rollup summaries
  Resultant effects from line pressure
  Jan 1st 2018 to present
Understand & capture contract violations automatically
  Exceed contract thresholds
Generate weekly reports for management
  More data for meetings with third parties
Multi-disciplinary team workshop
  Attack the things APC controls
Incorporate physics based models
  What if scenarios for line pressure

## Slide 23: Questions